| Illustrated Report For Radiant |  |  | Parameters | Avg | Min | Max | Dev |  |  | Facets azimuths |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Polished Radiant | 14.03.2009 |  |  | Crown height: Side, % | 11.63 | 11.19 | 12.20 | 1.01 |  |  |  |  |
|  |  |  |  | Crown height: Joint, % | N/A | N/A | N/A | N/A |  |  |  |  |
| Model | Simple |  |  | Pavilion height: Side, % | 49.54 | 49.24 | 49.86 | 0.62 |  |  |  |  |
| Expert name | Makoed A.G. |  |  | Pavilion height: Joint, % | N/A | N/A | N/A | N/A |  |  |  |  |
| Real weight, ct |  |  |  | Table: Side, % | 71.91 | 68.12 | 75.70 | 7.58 |  |  |  |  |
| Calculated weight, ct | 0.52, 0.5196 |  |  | Table: Corner w.r.t. Corner, % | 76.69 | 76.41 | 76.97 | 0.56 |  |  |  |  |
| Spread | 0.05 ct, 8.22 % |  |  | Table: Corner w.r.t. Width, % | 108.34 | 108.23 | 108.45 | 0.22 |  |  |  |  |
| Extra Facet / Nat | Yes (1) |  |  | Diameter: Corner, % | 141.27 | 140.62 | 141.93 | 1.30 |  |  |  |  |
|  |  |  | Girdle thickness: Side, % | 2.44 | 2.17 | 2.76 | 0.59 |  |  |  |  |
| Width | Length | Ratio (L/W) | Corner Ratio | Diameter Minimum | Diameter Maximum |  |  | Girdle thickness: Joint, % | N/A | N/A | N/A | N/A |  |  |  |  |
|  |  |  |  |  |  |  |  | Corner angle width, % | 15.17 | 14.05 | 16.30 | 2.25 |  |  |  |  |
| 4.228 mm | 5.531 mm | 1.308 | 1.009 | 4.228 mm | 6.253 mm |  |  | Corner angle length, % | 15.05 | 13.62 | 16.66 | 3.04 |  |  |  |  |
|  |  |  |  |  |  |  |  | Culet, % | 0.61 | 0.33 | 0.82 | 0.49 |  |  | Facets heights (%) |
|  |  |  | Crown 1 Main Width height, % | 7.21 | 7.02 | 7.40 | 0.39 |  |  |  |  |
| Total height | Crown height: Side | Pavilion height: Side | Table: Side | Girdle: Side | Culet |  |  | Crown 1 Main Length height, % | 7.39 | 7.07 | 7.71 | 0.63 |  |  |  |  |
|  |  |  |  |  |  |  |  | Crown 1 Corner height, % | 7.26 | 6.87 | 7.85 | 0.98 |  |  |  |  |
| 2.690 mm 63.61 % | 0.492 mm | 2.094 mm | 3.534 mm | 0.103 mm | 0.026 mm |  |  | Crown 2 Main Width height, % | 4.48 | 4.36 | 4.59 | 0.22 |  |  |  |  |
|  |  |  |  |  |  |  |  | Crown 2 Main Length height, % | 4.58 | 4.50 | 4.66 | 0.16 |  |  |  |  |
|  |  |  | Crown 2 Corner height, % | 4.68 | 4.57 | 4.82 | 0.25 |  |  |  |  |
|  |  |  |  |  | Pavilion 1 Main Width height, % | 25.71 | 24.22 | 27.20 | 2.98 |  |  |  |  |
|  |  |  |  |  | Pavilion 1 Main Length height, % | 22.58 | 21.88 | 23.29 | 1.41 |  |  |  |  |
|  |  |  |  |  | Pavilion 1 Corner height, % | 45.57 | 44.91 | 46.20 | 1.29 |  |  |  |  |
|  |  |  |  |  | Pavilion Halves Width 1 height, % | 49.09 | 48.67 | 49.28 | 0.61 |  |  |  |  |
|  |  |  |  |  | Crown 1 Main Width angle, ° | 44.98 | 44.84 | 45.12 | 0.28 |  |  |  |  |
|  |  |  |  |  | Crown 1 Main Length angle, ° | 44.86 | 44.32 | 45.40 | 1.07 |  |  |  |  |
|  |  |  |  |  | Crown 1 Corner angle, ° | 45.00 | 44.86 | 45.18 | 0.32 |  |  | Girdle facets angles & MIC | Girdle facets azimuths & MIC |
|  |  |  |  |  | Crown 2 Main Width angle, ° | 27.13 | 27.12 | 27.13 | 0.01 |  |  |  |  |
|  |  |  |  |  | Crown 2 Main Length angle, ° | 27.51 | 27.15 | 27.88 | 0.72 |  |  |  |  |
|  |  |  |  |  | Crown 2 Corner angle, ° | 27.55 | 27.17 | 27.84 | 0.67 |  |  |  |  |
|  |  |  |  |  | Crown Star Width height, % | 4.35 | 4.22 | 4.49 | 0.27 |  |  |  |  |
|  |  |  |  |  | Crown Star Length height, % | 4.41 | 4.37 | 4.45 | 0.08 |  |  |  |  |
|  |  |  |  |  | Crown Star Width angle, ° | 20.38 | 19.26 | 21.36 | 2.10 |  |  |  |  |
|  |  |  |  |  | Crown Star Length angle, ° | 21.37 | 20.82 | 22.58 | 1.76 |  |  |  |  |
|  |  |  |  |  | Pavilion 1 Main Width angle, ° | 57.14 | 54.32 | 59.95 | 5.63 |  |  |  |  |
|  |  |  |  |  | Pavilion 1 Main Length angle, ° | 58.85 | 58.82 | 58.87 | 0.05 |  |  |  |  |
|  |  |  |  | Pavilion 1 Corner angle, ° | 35.72 | 34.79 | 36.57 | 1.79 |  |  |  |  |
|  |  |  |  | Pavilion Halves Width 1 angle, ° | 35.65 | 34.79 | 36.52 | 1.73 |  |  |  |  |
|  |  |  |  | Girdle facet angle, ° | 87.85 | 85.43 | 89.50 | 4.06 |  |  |  |  |
|  |  |  |  | Facets angles |  |  |  | Girdle asymmetry, girdle sides & internal angles |
| Appraiser title | AGS_2005 |  |  |  |  |  |  |  |  |
| Overall cut quality | N/A |  |  |  |  |  |  |  |  |
| Symmetry appraiser title | Internal |  |  |  |  |  |  |  |  |
| Overall symmetry quality | PR |  |  |  |  |  |  |  |  |
| Color |  |  |  |  |  |  |  |  |  |
| Clarity |  |  |  |  |  | Girdle center |  | Culet center |  | Тable center |  | MIC center |  |  |  |  |
| Polish |  |  |  | Girdle-Culet offset by table axis | 1.60 ± 0.29, % | 0.068 ± 0.012, mm |  |  |  |  |
|  |  |  |  | Girdle-Table offset by table axis | 0.90 ± 0.26, % | 0.038 ± 0.011, mm |  |  | Width-wise culet shift ratio (by width) | 2.207 mm, 52.21 % | 2.021 mm, 47.79 % |
| Fluorescence |  |  |  | Table-Culet offset by table axis | 2.29 ± 0.31, % | 0.097 ± 0.013, mm |  |  | Length-wise culet shift ratio (by width) | 2.721 mm, 64.36 % | 2.815 mm, 66.57 % |
|  |  |  |  | Girdle to table-culet line offset | 0.57 %, 0.024 mm |  |  | Length-wise culet shift ratio (by length) | 2.721 mm, 49.19 % | 2.815 mm, 50.89 % |